SModelS 3.0
Generalized Topologies
With Graphs
André Lessa

---
Goal
Describe signal topologies with arbitrary shapes, such as:
Ressonant production
Associated Production
R-Parity Violating Decays
Non-Z2 decays
...

---
Current Status – SModelS 2.0
Signal topologies (simplified models) are described by Elements:
list
Branch
.branches
Element
Particle
list
.weight
.oddParticles
.evenParticles
.Z2parity
.mass
list
list
...
ParticleList
.particles

---
Current Status – SModelS 2.0
Overall structure:
.branches = [Branch1, Branch2]
Element
.weight
.oddParticles = [Particle1, Particle2,...]
Branch
.evenParticles = [ParticleList1, ParticleList2,...]
.particles = [Particle1, Particle2,...]
ParticleList

---
Current Status – SModelS 2.0
Inclusive objects:
Branch
.branches
Element
Particle
.weight
.oddParticles
.evenParticles
.Z2parity
.mass
InclusiveBranch
...
.oddParticles = * (optional)
MultiParticle
.evenParticles = *
.particles
When comparing against branches:
Checks if last BSM particle matches (if defined)
Checks if intermediate BSM particles matches (if defined)
Ignores evenParticles
Ignores branch topology (number of vertices,...)
When comparing against particles:
Checks if any particle in .particles matches

---
Current Status – SModelS 2.0
Element comparison takes place when:
Decomposing the model
(equal elements have their weights combined)
Matching against the database
(uses inclusive objects)

---
Current Status – SModelS 2.0
Element comparison: ElementA = ElementB?
BranchA
.branches
ElementA
ParticleA
.weight
.oddParticles
.evenParticles
ParticleListA
(any branch ordering)
(any particle ordering)
BranchB
.branches
ElementB
ParticleB
.weight
.oddParticles
.evenParticles
ParticleListB

---
Current Status – SModelS 2.0
A lot of the SmodelS structure is based on the 2-branch/Z2 assumption
However, it only affects the inner layers (Element class and its methods)
How to move towards general topologies? → Graphs

---
Using Graphs to Describe Topologies
Nodes = Particles
PV
Directed Graph
(Directed Rooted Tree)
Edges = “Decay”
Can describe any topology
Well stablished libraries (networkx, ...)

---
Implementation
Main steps:
Text description ↔ graph ✓
Graph comparison ✓
Element compression ✓
Decomposition ✓
Inclusive objects ✓
Extracting relevant information from graphs (database) ✓
New database format (how to store data) ✓
Simplified missing topologies ✓
Printers ✓
...

---
Strings ↔ Graphs
We can use MadGraph-like language to convert the graphs to text and vice-versa:
(PV → anyBSM(1), anyBSM(2)), (anyBSM(1) → e+, anyBSM(3), anyBSM(4) ), (anyBSM (2) → e-, nu, anyBSM(5) ) , (anyBSM(3) → nu,MET), ....
We can use particle labels if we want to specify quantum numbers (as it is currently being done)
We would like to keep some backward compatibility → convertion to/from bracket notation (for 2-branch/Z2 elements)

---
Strings ↔ Graphs

---
SModelS 3.0 – Simplified Model Topologies
In v3 “Elements” are renamed SMS (simplfied model spectra).
Three types of SMS are defined:
GenericSMS
a base class implementing common features of graphs
TheorySMS
class derived from GenericSMS and is used to describe SMS from the BSM model (generated by decomposition)
ExpSMS
class derived from GenericSMS and used to describe database simplified models

---
SModelS 3.0 – Simplified Model Topologies
The main differences between TheorySMS and ExpSMS are:
TheorySMS objects can be sorted and do not contain inclusive nodes
The comparison of TheorySMS objects is straightforward (since it can be sorted)
ExpSMS objects can NOT be sorted and can contain inclusive nodes
(however, ExpSMS can put in a standard format, so two identical SMS defined in the database with distinct node orderings are stored in the same way)
The comparison between ExpSMS and other SMS objects allows for any node ordering

---
SModelS 3.0 - TheorySMS
Signal topologies from the BSM decomposition are described by TheorySMS topologies:
PV
P
P
Particle
ParticleNode
.mass
.totalwidth
.particle
.nodes
._isSM
...
.nodeIndices
.isFinal
TheorySMS
.canonName
(derived from GenericSMS)
.weightList
...
Used to identify SM particles

---
TheorySMS Comparison
Comparing SMS is no longer simple, since we have arbitrary shapes (topologies).
But it can still be done in 2 steps:
Shape (topology) matching
Particle comparison
=?

---
TheorySMS Comparison
Shape (topology) matching:
=?
The above shapes are equivalent, since the ordering of the nodes in each decay is irrevalant.
Easy using canonical labels (names)!

---
Canonical Name
We define the canonical (topology) label as:
i) For each final node (leaf):
Similar to a nested bracket notation! (1 → left bracket, 0 → right bracket)
Name → 10
ii) For each decayed node:
Name → 1 (sorted daughters name) 0
iii) Build name recursively → Graph name = PV name
Examples:
1 10 10 110100 0
1 10 10 0
1 10 10 0
10
10
10
10
10
10

---
Canonical Name
Example:
10
10
10
10
10
10
1 10 10 110100 0
1 10 11010100 0
10
1 10 10 0
=?
1 10 10 10 0
10
10
10
1 10 10 110100 0
1 10 11010100 0
10
10
1 10 10 0
1 10 10 10 0
10
10
10
10
Name 1:
1 110101101000 110110101000 0
Name 2:
1 110101101000 110110101000 0
Name 1 = Name 2

---
Canonical Name
The canonical name can also be used to sort the nodes from the same parent and structure the tree in a default format
1 10 10 0
1 10 10 0
→
1 10 10 110100 0
1 10 10 110100 0
1 1010 0
1 1010 0
10
10
10
10
10
10
10
10
10
10
10
10
For equivalent nodes (same name) we sort according to particle and then daughter nodes

---
Compressing TheorySMS
How to define mass and invisible compression?
It has to be applied node by node!
Invisible Compression
Node X is compressed if:
All its daughters are invisible
All its daughters are “final states”
X decays promptly or is invisible
→
X
X

---
Compressing TheorySMS
Mass Compression
Y
Node X is compressed if:
decays promptly
decays to a single BSM particle
and
Y
→
X
A
A
m_X - m_A < \Delta m

---
Decomposition
Decomposition follows a similar algorithm, but generalized to deal with arbitrary graphs.
First, starting with the model (production cross-sections and particles), create all simple SMS of the form:
PV
PV
PV
...
A
X
A
B
Y
A
Only SMS with cross-sections larger than sigmacut are kept
\sigma\left(pp \to A+B\right)
\sigma\left(pp \to X+Y\right)
\sigma\left(pp \to A+A\right)

---
Decomposition
For a given initial SMS:
Iterate over the “final states”
For each final state construct all possible decays (including possible stable state)
Add all decays to original SMS
Apply step 1) to all SMS created by the last step
...
...

---
Decomposition
Nodes can be tagged with the attribute “.isFinalState = True” to avoid further decays
The SMS has the attributes:
prodXSec = list of production cross-sections (distinct sqrts) for PV
maxWeight = maximum weight (largest production cross-section times BRs)
decayBRs = total BR (product of BRs appearing in the SMS)
PV
A
B
\sigma
{\small BR(A\to...)}
{\small BR(B\to...)}
w = \sigma \times BR(A \to ...) \times BR(B \to..) ...

---
Decomposition
During step 3) any SMS with maxWeight smaller than sigmacut is ignored
...
In the end only SMS where all final state nodes have finalStates = True are kept (avoids intermediate undecayed trees generated by failing to pass sigmacut)
There is a lot of duplicated steps in the decompositon, since everytime a particle appears all of its possible decay trees have to be generated again. For instance, pair production of the same particle will generate exactly the same decay branches twice. However, since the possible decays are filtered by sigmacut, it depends on which position the particle appears (how small is the weight leading to the particle). Therefore previously generated cascade decays (under some effective sigmacut assumption), can not be easily recycled.
→ A better solution still to be found?
w < \sigma_{\mbox{cut}}
w > \sigma_{\mbox{cut}}

---
SModelS 3.0 - ExpSMS
Simplified model topologies used for defining experimental results are described by ExpSMS topologies:
P
P
PV
Particle/
MultiParticle
ParticleNode/
InclusiveParticleNode
.eCharge
.colordim
.nodes
._isSM
...
.particle
.nodeIndices
ExpSMS
.isInclusive
.canonName
(derived from GenericSMS)
.inclusiveList
No mass and totalwidth is defined for database particles
Used to tag inclusive nodes

---
SModelS 3.0 - ExpSMS
Unlike TheorySMS topologies, ExpSMS topologies can hold inclusive nodes and inclusive particle definitions (multiparticles).
ExpSMS can be generated from strings (as appearing in TxNames constraints and conditions)
Experimental topologies can not be sorted (their node ordering has to match the data ordering in the TxName).
Experimental topologies can be matched to other (ExpSMS or TheorySMS) topologies.
The matching has to take into account inclusive node and particle definitions and all possible node orderings.
The matching is done in two steps:
Shape (topology) matching (for ExpSMS containing inclusive nodes, the shape is not defined and will match any other shape)
Particle matching (must take into account any node ordering and inclusive nodes)

---
ExpSMS Matching
Shape (topology) matching:
Simple comparison of canonical names
If the ExpSMS contains an inclusive node, its canonical name is defined as “*” and will match any canonical name.

---
ExpSMS Matching
Particle/Node Matching
=?
Two nodes match if:
Their particles and canonical names match
Their daughter nodes match
Two SMS match if their root nodes match, which means the SMS have matching canonical names and all nodes have matching nodes.

---
ExpSMS Matching
Particle/Node Matching
When matching two sets of daughters from the nodes being compared, the following procedure is adopted:
SMS A
SMS B
Node 2 =? Node a
Node 2
Node a
d
e
6
7
c
8
All possible pairs of daughters are compared:
6
c
(to improve perfomance, it is only necessary to compare nodes with the same canonical name)
d
7
8
e

---
ExpSMS Matching
Particle/Node Matching
A bipartite graph is constructed where the left nodes are the daughters for SMS “A”, the right nodes the daughters from SMS “B” and the edges connect the pairs of daughter nodes which have matched.
6
c
d
7
8
e
A maximal matching algorithm is used to determine the maximal number of matchings (edges which do not share common nodes)
6
c
6
c
d
d
7
7
8
8
e
e
maximal matching = {6 : c, 7 : d, 8 : e}

---
ExpSMS Matching
Particle/Node Matching
If all left nodes and right nodes have had matches, the daughter nodes are considered as matched and the matching dictionary is kept
6
c
Daughters match
d
7
8
e
maximal matching
 Otherwise the daughters are NOT matched:
6
c
Daughters do not match
d
7
8
e
maximal matching
With this procedure, the SMS matching checks for any possible node ordering.

---
ExpSMS Matching
This algorithm requires many node comparisons
If more than one ordering matches we keep the “first one” (arbitrary)
In v2 we already have this issue, but it is simpler:
only two possible branch orderings
in a given vertex we compare ParticleLists (SM particles) and cache the comparison result
→ A better solution still to be found?

---
Inclusive Objects – SModelS v2
In SModelS v2 we make use of
Inclusive Particles: matches any particle
Inclusive Branches: matches other branches (may or may not include comparison of intermediate and final BSM states)
Any (single) SM final state:
(InclusiveParticle → [[‘*’]])
*
Y
X
Any arbitrary number of SM particles:
(InclusiveBranch→ [‘*’] + intermediate and final states defined)
*
Y
X
Arbitrary SM final states and BSM intermediate states:
(InclusiveBranch→ [‘*’] + final states defined)
Z
*
Arbitrary SM final states and BSM states
(InclusiveBranch→ [‘*’])
*

---
Inclusive Objects – SModelS v3
In v3 inclusive objects are handled using three new definitions:
Final states of X = A,B,a,b
Final States of a node: particles appearing as a final state (undecayed) generated by the cascade decay of the node
X
A
B
C
Inclusive Node:
Has pre-defined finalStates
Matches any node if all the final states of the node match at least one of the final states of the inclusive node
Its canonName is an inclusive value (*), which matches any int
If a tree contains an InclusiveNode, all of its antecessors also have their canonNames set to *
It is represented in string form by “Inclusive > final states” or by [‘*’] (old bracked notation)
a
b
Inclusive
(final states)

---
Inclusive Objects – SModelS v3
InclusiveList Node:
Behaves as a regular ParticleNode, however it represents any repeated number of the same particle
It is represented in string form by *particleLabel (e.g. *q) → can only be implemented using the new string format
When matching to another list of nodes, it will match all the nodes which match its particle:
X
A
B
*C
=
X
X
A
*C
A
C
C
C

---
Inclusive Objects – SModelS v3
Examples:
PV
Matches any node/branch which only leads to SM and MET final states
canonName = *
Inclusive
(anySM,MET)
canonName = *
...
finalStates = [anySM,MET]
PV
canonName = *
canonName = *
...
Matches any node which cascade decays to SM final states
Inclusive
(anySM)
PV
canonName = *
Matches any node which decays to X plus any number of SM particles
...
X
*anySM

---
Inclusive Objects – SModelS v3
The inclusive objects in v2 correspond to:
*
X
Y
Y
anySM
X
X
*
Y
*anySM
Y
X
Inclusive
(anySM,Z)
Z
*
Inclusive
(anySM, anyBSM)
*

---
Database Topologies
How to store information (effs, ULs) for arbitrary topologies?
Numbered nodes
dataMap → maps the nodes attributes to a flat array
TxName.dataMap = {arrayIndex : (node number, attribute, unit),...}
flat array index
6
1
3
DataMap = {0 : (1, ‘mass’, GeV), 1 : (3, ‘mass’,GeV), …
…, 6 : (12, ‘mass’, GeV),
     7 : (12, ‘totalwidth’, GeV)}
8
None
2
None
7
9
10
11
12
4
5
BSM nodes: 1,3,4,6,7,8,12

---
Database - dataMap
The dataMap holds all the information for extracting the relevant data from a TheorySMS.
Inclusive nodes are ignored (do not appear in a dataMap)
When creating a database entry, the dataMap can be directly defined in the TxName.txt file, as well as the flat data points:
constraint : {(PV > anyBSM(1),anyBSM(2)), ...}
dataMap : {arrayIndex : (node number, attribute, unit),…}
EfficencyMap: [ [[m1,m2,…],eff], [[m1’,m2’,…],eff’, ...]
flat data array of floats (without units)
The node numbers are defined by the particle indices appearing in the constraint:
constraint : {(PV > anyBSM(1),anyBSM(2)), ...}
node = 2
node = 1

---
Database - dataMap
For the old format (nested brackets) an intermediate map is constructed, which maps the nested bracket indices to a flat array:
arrayMap : {arrayIndex : ((i,j,k), attribute, unit, node number),…}
flat array index
i,j → indices of nested array
k → 0 for mass, 1 for width (if present in data)
Example:
[ [m0,(m1,w1)], [m2,(m3,w3)] ]
1
2
(SM)
(SM)
3
5
4
6
arrayMap : {0 : ((0,0,0), ‘mass’, GeV, 1), 1 : ((0,1,0), ‘mass’, GeV, 3),
        2 : ((1,0,0),’mass’, GeV, 2), 3 : ((1,1,0), ‘mass’, GeV, 4),
        4 : ((0,1,1), ‘totalwidth’, GeV, 3), 5 : ((1,1,1), ‘totalwidth’, GeV, 4) }

---
Database - dataMap
The arrayMap is used to convert the old data format to a flat array and construct the dataMap:
[m0,m1,m2,m3, w1, w3 ]
[ [m0,(m1,w1)], [m2,(m3,w3)] ]
arrayMap
dataMap : {... }
Hence the old format can be (internally) converted to a new flat array format with a well defined dataMap

---
Database - dataMap
Finally the dataMap can be used for extracting the required information from TheorySMS objects (from the decomposition):
ExpSMS
TheorySMS
matching
1
2
X
Y
(SM)
(SM)
3
5
4
6
Z
e-
Z
e+
Matched TheorySMS:
(When the ExpSMS constaints Inclusive nodes, these are used as replacements for the original TheorySMS nodes)
The matched SMS has its nodes numbered according to the ExpSMS numbering
X (1)
Y (2)
[mX,mZ,mY,mZ, wZ, wZ ]
dataMap : {... }
Z (3)
e-
Z (4)
e+

---
Database – matching
When matching TxNames with TheorySMS from decomposition:
The matching returns the SMS with the same shape (sorted) and the daugthers ordered in the way they have matched the txname SMS (ExpSMS)
The matched SMS nodes are numbered according to the txname SMS numbering
The matched SMS receives a label matching the label used for evaluating constraints.
Matched SMS (TheorySMS)
ExpSMS
TheorySMS
match
X (1)
Y (2)
1
2
X
Y
(SM)
(SM)
Z (3)
e-
3
5
Z (4)
e+
4
6
Z
e-
Z
e+
sms_1
sms_1

---
Database – Constraints and Conditions
The constraints and conditions are string expressions for the SMS weights:
v3 format
constraint: 2*({(PV > …} + { (PV > …)})
or
constraint: 2*([[[...]]]+ [[[...]]])
v2 format
v3 format
condition: Csim({(PV > …},{ (PV > …)})
or
condition: Csim([[[…]]], [[[...]]])
v2 format
Note that in v3 strings representing SMS are delimited by curly brackets:
{(PV > …} = {ExpSMS}

---
Database – Constraints
In v3 the SMS appearing within the constraints are converted to ExpSMS objects and receive labels, which are used as replacements in the string expressions. The constraint function (string) is also created using the labels:
constraint: 2*({(PV > …} + { (PV > …)})
or
sms_1
sms_2
constraint: 2*([[[...]]]+ [[[...]]])
constraintFunc = 2*(sms_1 + sms_2)
The SMS appearing in the constraints are required to be unique, which means that distinct ExpSMS belonging to the same TxName can not mach:
This restriction is needed in order to make sure that the same TheorySMS will not match more than one ExpSMS in the same constraint (to avoid double counting)
sms_1
sms_2
\neq

---
Database – Constraints
The SMS and respective labels appearing in constraints are stored in the TxName.smsMap:
smsMap = { : sms_1, : sms_2, ...
constraint
When checking if a TheorySMS appears in the TxName, the ExpSMS objects from smsMap are used for comparison. Since the TheorySMS has to match a single ExpSMS, it is “tagged” with the ExpSMS label:
TheorySMS
ExpSMS
the txlabel is then used to evaluate the constraints using the constraintFunc
X
Y
matching
X
Y
Z
e-
Z
e+
sms_2
Z
e-
Z
e+
Txlabel = sms_2

---
Database – Constraints
The constraints can then be evaluated using a dictionary mapping the TheorySMS weights to their txlabels.
In summary:
constraint: 2*({(PV > …} + { (PV > …)})
smsMap = {ExpSMS : sms_1,
        ExpSMS : sms_2, ...}
match
TheorySMS
constraintFunc = 2*(sms_1 + sms_2)
.txlabel = sms_1
.weight = w1
smsDict = {sms_1 : w1, sms_2 : w2}
eval(constraintFunc, smsDict)
value

---
Database – Conditions
Evaluating conditions are less straightforward, since they may contain overlapping SMS. For instance, in the example below the first SMS ([[[L,L]],[[L,nu]]]) contains the second:
conditions: Cgtr([[[L,L]],[[L,nu]]], 3*[[[L,L]],[[ta,nu]]]); Csim([[[L,L]],[[e,nu]]], [[[L,L]],[[mu,nu]]])
Therefore, for conditions, a smsMap is defined for each condition and the map can contain overlapping SMS.
In this case the TheorySMS can match multiple SMS and the ordering of each matched SMS does not have to be the same.
Therefore, when evaluating conditions, the SMS matched by the constraints are compared to the ones contained in conditions. If it matches, its weight is added to the matched sms label.

---
Conclusions
The implementation is somewhat encapsulated (it does not affect the higher levels of the code)
Graphs can be an useful tool
The main reamining issue is how to resolve ambiguities for equivalent nodes
Some functionality is already in place in smodels:graphs