SModelS 3.0
Generalized Topologies
With Graphs

---
Goal
Describe signal topologies with arbitrary shapes, such as:
Ressonant production
Associated Production
R-Parity Violating Decays
Non-Z2 decays
...

---
Current Status – SModelS 2.0
Signal topologies (simplified models) are described by Elements
list
Branch
.branches
Element
Particle
list
.weight
.oddParticles
.evenParticles
.Z2parity
.mass
list
...
ParticleList
list
.particles

---
Current Status – SModelS 2.0
Overall structure:
.branches = [Branch1, Branch2]
Element
.weight
.oddParticles = [Particle1, Particle2,...]
Branch
.evenParticles = [ParticleList1, ParticleList2,...]
.particles = [Particle1, Particle2,...]
ParticleList

---
Current Status – SModelS 2.0
Inclusive objects:
Branch
.branches
Element
Particle
.weight
.oddParticles
.evenParticles
.Z2parity
.mass
InclusiveBranch
...
.oddParticles = * (optional)
MultiParticle
.evenParticles = *
.particles
When comparing against branches:
Checks if last BSM particle matches (if defined)
Checks if intermediate BSM particles matches (if defined)
Ignores evenParticles
Ignores branch topology (number of vertices,...)
When comparing against particles:
Checks if any particle in .particles matches

---
Current Status – SModelS 2.0
Element comparison takes place when:
Decomposing the model
(equal elements have their weights combined)
Matching against the database
(uses inclusive objects)

---
Current Status – SModelS 2.0
Element comparison: ElementA = ElementB?
BranchA
.branches
ElementA
ParticleA
.weight
.oddParticles
=
.evenParticles
ParticleListA
=
(any branch ordering)
BranchA
.branches
ElementA
ParticleA
.weight
.oddParticles
.evenParticles
ParticleListA

---
Current Status - SModelS
However, for each decay: i → j
*for simplicity we will consider 2-body decays for now
Model and event dependent
SModelS
Model dependence
How can we improve on this zero order approximation?
M_i,\; \Gamma_i
M_j,\; \Gamma_j
m_j
\beta_j = \beta_j(\beta_i,M_i,M_j,m_j,\theta,\phi)
\langle \beta_j \rangle = \int d \beta_{i} \int d\Omega\; P(\beta_i,\theta,\phi) \beta_j \Rightarrow \langle \beta_j \rangle = \langle \beta_j \rangle (M_i,M_j,m_j)
\textcolor{red}{\langle \beta_j \rangle \simeq 0.8}

---
Analytical Approximation
Main Goals:
Obtain an approximation for the average boost for each step in the cascade decay
The approximation can only depend on the masses and element topology
The calculation has to be very fast (it is done many times within the code)
Algorithm:
analytical approx.
analytical approx.
Pre-computed
(approximated)
M_0,\; \Gamma_0
M_1,\; \Gamma_1
m_1
m_2
M_2,\; \Gamma_2
\textcolor{red}{\langle \beta_0 \rangle (M_0)}
\langle \beta_1 \rangle( \langle \beta_0 \rangle,M_0,M_1,m_1)
\langle \beta_2 \rangle( \langle \beta_1 \rangle,M_1,M_2,m_2)

---
 Approximation – Single Decay
Assumptions:
random (equally probable) angles (in the mother's CM)
2-body decay
average boost = boost of average:
It is a good approximation if P is ~flat on the angles and ~peaked at the average mother boost
In practice it is better to directly compute:
M_0,\; \beta_0
M_1, \beta_1
m_1
\begin{eqnarray*} \langle \beta_1 \rangle_{\mbox{exact}} & = & \int d \beta_{0} \int d\Omega\; P(\beta_0,\theta,\phi) \beta_1(\beta_0,\theta,\phi) \\ \to \langle \beta_1 \rangle_{\mbox{approx}}& = & \frac{1}{4 \pi} \int d\Omega \; \beta_1(\langle \beta_0 \rangle, \theta,\phi) \end{eqnarray*}
\langle \gamma_1 \beta_1 \rangle =\frac{1}{4 \pi} \int \gamma_1 \beta_1(\langle \gamma_0 \beta_0 \rangle, \theta,\phi) d\Omega
\theta, \; \phi \to \mbox{ CM angles}

---
 Approximation – Single Decay
In the mother's CM:
In the lab frame (boost along z)
*the axis is arbitrary and does not correspond to the beam line
M_0,\; \beta_0
M_1, \beta_1
m_1
E_1^{cm}=\frac{M_0^2+M_1^2-m_2^2}{2M_0}
|\vec{P}_1^{cm}|=P_1^{cm} = \sqrt{(E_1^{cm})^2-M_1^2}
\begin{eqnarray*} P_{1x}' & = & P_1^{cm}\cos{\phi}\sin{\theta} \\ P_{1y}' & = & P_1^{cm}\sin{\phi}\sin{\theta} \\ P_{1z}' &= & \gamma_0(P_1^{cm}\cos{\theta}+\beta_0 E_1^{cm})\\ E_1' & = & \gamma_0(E_1^{cm}\cos{\theta}+\beta_0 P_1^{cm}) \end{eqnarray*}
\gamma_1 \beta_1 = \frac{P_1'}{M_1} = \frac{\sqrt{x^2-\bar{M}_1^2}}{\bar{M}_1}
x \equiv E_1^{cm} + \beta_0 P_1^{cm} \cos\theta \mbox{ and } \bar{M}_1^2 \equiv \frac{M_1^2}{\gamma_0^2}

---
 Approximation – Single Decay
Finally, taking the average over the angles:
The above analytical expression depends only on the masses and the mother's velocity
We define an “average boost” as:
Used for computing
\langle \gamma_1 \beta_1 \rangle = \frac{1}{2 \beta_0 P_{1}^{cm}} \int_{x_-}^{x_+} \frac{\sqrt{x^2-\bar{M}_1^2}}{\bar{M}_1} dx
x_{\pm} \equiv E_1^{cm} \pm \beta_0 P_1^{cm}
\Rightarrow \textcolor{red}{ \langle \gamma_1 \beta_1 \rangle =\frac{\bar{M}_1}{4\beta_0 P_1^{cm}}[\frac{x\sqrt{x^2-\bar{M}_1^2}}{\bar{M}_1^2}-\ln{(\frac{|x+\sqrt{x^2-\bar{M}_1^2}|}{\bar{M}_1}})]|^{x_+}_{x_-}}
\langle \beta_{1} \rangle=\frac{\langle \gamma_1 \beta_1 \rangle}{\sqrt{1+\langle \gamma_1 \beta_1 \rangle^2}}
\langle \gamma_2 \beta_2 \rangle

---
 Approximation – Single Decay
Finally, taking the average over the angles:
The above analytical expression depends only on the masses and the mother's velocity
We define an “average boost” as:
Used for computing
\langle \gamma_1 \beta_1 \rangle = \frac{1}{2 \beta_0 P_{1}^{cm}} \int_{x_-}^{x_+} \frac{\sqrt{x^2-\bar{M}_1^2}}{\bar{M}_1} dx
x_{\pm} \equiv E_1^{cm} \pm \beta_0 P_1^{cm}
\Rightarrow \textcolor{red}{ \langle \gamma_1 \beta_1 \rangle =\frac{\bar{M}_1}{4\beta_0 P_1^{cm}}[\frac{x\sqrt{x^2-\bar{M}_1^2}}{\bar{M}_1^2}-\ln{(\frac{|x+\sqrt{x^2-\bar{M}_1^2}|}{\bar{M}_1}})]|^{x_+}_{x_-}}
\langle \beta_{1} \rangle=\frac{\langle \gamma_1 \beta_1 \rangle}{\sqrt{1+\langle \gamma_1 \beta_1 \rangle^2}}
\langle \gamma_2 \beta_2 \rangle

---
 Approximation – 3-body Decay
All the results were obtained assuming a 2-body decay
However a 3-body decay can be viewed as a 2-body decay with variable mass:
We can approximate the 3-body decay by a 2-body decay with an “effective mass”:
M_0,\; \beta_0
M_1, \beta_1
m_a
m_b
\sim
M_0,\; \beta_0
M_1, \beta_1
m_1
m_1^2 = (p_a+p_b)^2 = m_{ab}^2
m_a + m_b < m_1 < M_0 - M_1
m_1 \to m_1^{eff} = \frac{1}{2}\left(m_1^{max}+m_1^{min}\right) = \frac{1}{2} \left(M_0 -M_1 + m_a + m_b\right)

---
 Analytical Approximation
With the results obtained and the initial average boost we can compute all the cascade decay boosts:
...
...
How to determine the initial (hard collision) boost?
M_0,\; \Gamma_0
M_1,\; \Gamma_1
m_1
m_2
M_2,\; \Gamma_2
\textcolor{red}{\langle \beta_0 \rangle (M_0)}
\langle \gamma_1 \beta_1 \rangle( \langle \beta_0 \rangle,M_0,M_1,m_1)
\langle \gamma_2 \beta_2 \rangle( \langle \beta_1 \rangle,M_1,M_2,m_2)

---
Backup